## Slide 1: CAMFAS: A Compiler Approach to Mitigate Fault Attacks via Enhanced SIMDization
Zhi Chen1, Junjie Shen1, Alex Nicolau1, Alex Veidenbaum1
Nahid Farhady Ghalaty2 and Rosario Cammarota3
1University of California, Irvine
2Accenture Cyber Security Technology Labs, Virginia, USA
3Qualcomm Research, San Diego, USA

## Slide 2: Fault Attacks
Fault attacks occur as intentional disturbance of a micro-processor
  To exploit the secret keys of crypto modules.
  To take control of the micro-processor actions.

## Slide 3: Fault Attack Process
Fault attack vectors include two main steps:
  Fault measurement – the process to get faulty data
    Fault Injection.
    Fault effect observation.
  Fault analysis – techniques to process faulty and unaltered information
    E.g., DFA, DFIA.

## Slide 4: Fault Attack Countermeasures
Fault attack countermeasures attempt to prevent an attacker from observing the effect of injected faults.
  Shielding to physically block fault injection
  Sensors to detect fault injections
    E.g., temperature, EM, voltage anomaly sensors.
  Redundancy for fault detection
    E.g., error-correcting codes (hardware), multi-versioning (software).

## Slide 5: Motivation
Hardware countermeasures
  Overhead impact silicon area and performance.
  Increase the hardware design life cycle.
  Limited flexibility.
Software countermeasures (timing and spatial code redundancy)
  Overhead impact memory footprint, code size, and register pressure, i.e., performance
    E.g., run crypto algorithm twice, duplicate instructions
  Tedious and error-prone deployment of the countermeasures.
  Highly flexible.
Type | Overhead | Cost | Flexibility | Efficacy
Hardware | High | High | Low | High
Software | High | Moderate | High | Low
Table 1: Existing countermeasures on a yardstick.
Recent research has shown that multiple fault injections can break redundancy techniques in algorithm or instruction level - refer to Yuce et al. in FDTC’16

## Slide 6: CAMFAS
Rationale
  Rely on the mechanism of automatic vectorization (SIMDization) to convert instruction duplication into vector operations.
  Vector units are ubiquitous in modern micro-processors
    Intel x86 – SSE, AVX
    ARM - NEON
Expected outcome
  Reduced performance penalty compared to instruction duplication.
  Elevated fault coverage due to a reliable insertion of the mitigation with an enhanced version of the auto-vectorizer of the compiler: CAMFAS.

## Slide 7: CAMFAS Framework
ALU instructions: Duplicated and their data is placed in SIMD registers.
Memory instructions: Memory addresses are duplicated using gather and scatter.
Branches: Condition computation is duplicated. PC update is not checked.
Calls: Function calls are not duplicated, but some library calls are duplicated if they have the equivalent SIMD prototypes in LLVM IR (e.g. sqrt, pow, etc.).

## Slide 8: ALU Instruction Duplication
B
B’
C
C’
Replicate
A’ = B’ + C’
A = B + C
Shuffle
+1/0/-1
+1/0/-1
Compare
A’ = B’ + C’
A = B + C
Vector operation
There is an error if one of the fields is non-zero
Original
B
C
A

## Slide 9: Memory Instruction Duplication
Only addresses are protected.
  Load instruction: gather.
  Store instruction: address is checked before store.
Data can also be checked at the cost of more overhead
Original: D = Mem[A]
...
Memory
D
D’
Gather
Addr: A
Addr: A’

## Slide 10: Error Checking Insertion
Shuffle + Compare.
Error checking code only inserted at selected positions to reduce the performance overhead.
  Before stores.
  Before function calls.
  Before conditional branches.
A==A’
A’==A
A’
A
A
A’

## Slide 11: Fault Injection Simulation
Use Pin tool to collect dynamic instruction trace.
Randomly pick a fault position in trace file.
  Pick an instruction
  Flip the chosen bit
Repeat fault injection 1000 times for each crypto algorithm.
Crypto
algorithm
ip1, regs_i, regs_o
ip2, regs_i, regs_o
ip3, regs_i, regs_o
…
ipn, regs_i, regs_o
Pin Tool
Trace File
Rand(1, n)
ip1, regs_i, regs_o
ip2, regs_i, regs_o
ip3, regs_i, regs_o
…
ipn, regs_i, regs_o
1 | 0 | 0 | … | 1 | 0
Rand(regs_i)
Regs_i[1]
Rand(0, 31)
1 | 0 | 0 | … | 1 | 0
   pick a register
   pick a bit
1 | 0 | 0 | … | 0 | 0

## Slide 12: Evaluation
CAMFAS can also be applied to other micro-processors support vector extensions.
  e.g. ARM processors w/ NEON
Experimental Platform | 
CPU | Intel Xeon PhiTM 7210 with AVX-512 SIMD extension
Memory | 16GB
OS | Ubuntu Server 16.04 with Linux-4.4.0 kernel
Compiler framework | LLVM 4.0
Target | Libgcrypt-1.7.6

## Slide 13: Cipher Execution Results
Detected: program terminates due to fault being detected.
Incomplete: execution fails without generating attackable output.
Masked: program completes normally and produces correct output.
Corrupted: program completes normally and produces faulty output.
The fault provides useful information to an attacker for its fault analysis step

## Slide 14: Fault Coverage
N: No fault detection
O: CAMFAS without memory protection
W: CAMFAS with memory protection
Almost full coverage
with memory protection!
The remaining corrupted cases are mainly caused by faults injected to error checking code

## Slide 15: Performance overhead
With memory protection: 2.2x.
Without memory protection: 1.7x.

## Slide 16: Discussion
Differential Fault Analysis (DFA)
  Requires both correct and faulty cipher texts.
  CAMFAS detects incorrect result and prevents the generation of faulty cipher text.
Differential Fault Intensity Analysis (DFIA)
  Relies on the bias of fault behavior.
  CAMFAS effectively prevents faulty output from being propagated.
Single-Glitch Attack
  Injects clock glitches at precisely controlled timing and pipeline stages to thwart redundancy-based countermeasures
  CAMFAS makes the attack more difficult as duplication and error checking are inserted at the IR level

## Slide 17: Conclusions
CAMFAS is a redundancy-based countermeasure implemented in LLVM infrastructure.
CAMFAS exploits SIMD units in modern micro-processors to mitigate fault attacks.
CAMFAS provides high fault coverage while keeps a moderate performance penalty.
Future directions
Extend CAMFAS to thwart side-channel attacks.
New micro-architectural features to mitigate fault attacks.

## Slide 18
Thank you!

## Slide 19: Backup Slides

## Slide 20: Fault injections can be detrimental
Methods: Laser, EM, heat, etc.
Common approach: Differential Fault Analysis (DFA)
A single fault is enough to break the cryptosystem
  Public key cipher: “Bellcore attack” on RSA-CRT [1]
  Block cipher: DFA on AES [2]
[1] Boneh, Dan, Richard A. DeMillo, and Richard J. Lipton. "On the importance of eliminating errors in cryptographic computations." Journal of cryptology 14, no. 2 (2001): 101-119.
[2] Tunstall, Michael, Debdeep Mukhopadhyay, and Subidh Ali. "Differential fault analysis of the advanced encryption standard using a single fault." IFIP International Workshop on Information Security Theory and Practices. Springer, Berlin, Heidelberg, 2011.

## Slide 21: RSA-CRT
RSA with Chinese Remainder Theorem implementation
Given:
  message , private exponent , primes , and
RSA signing:
RSA-CRT:
  Calculates and
  Four times faster than RSA

## Slide 22: Bellcore Attack
Run RSA-CRT twice with the same message
  Original and fault injected
If the fault was injected to :
  i.e., and
  Meaning , but
  Therefore,
  Based on and , where is the public exponent
  Calculated !